## Slide 1: Introduction:
Robot:
  This name was firstly used by a “Czechoslovakian” dramatist Karel Capek, 1921.
Aim:
  Robots were designed to be perfect and tireless workers who performed manual labor for human beings. Industrial robots were intended to help human workers, not to replace them.
Characteristics:
  Specialized machine tool: Consistent, unchanging, unthinking, untiring, hazardous jobs, and precise.

## Slide 2: Types of robots
Parallel Robot: Consists of a moving platform and a fixed base interconnected by several links.
  Examples:
6-DoF
3-DoF
Prismatic
joints
Universal
joints
Spherical
joints
Revolute
joints
Platform
Base

## Slide 3: Types of robots
Serial Robot: Consists series of links inter-connected by joints that extend from a base to an end-effector.
  Examples:
Revolute
joints
6-DoF

## Slide 4: Types of robots (Comparison)
Parallel Robot:
Higher load
Smaller workspace
Serial Robot:
Lower load
Bigger workspace
This course!

## Slide 5: Course Contents
Description of position and orientation
Direct kinematics (position)
Inverse kinematics
Kinematics (velocities, accelerations and static forces)
Dynamic analysis
Trajectory generation

## Slide 6: Preface:
Manipulators/Robots consist of rigid links, which are connected by joints. That are instrumented with position sensors, which measure the relative position of neighboring links.
Revolute joints  joint angles.
Prismatic joints  joint offset/displacement.
Robot base  joints  links  End-Effector (tool)
3D space (position & orientation)  6 DoF
1 joint  1 DoF  robot of 6 joints (at least)

## Slide 7
Chapter 2:
Description of position and orientation