---------------------------------------------------------------------------------------------------------------------------------------

#1	A three-phase synchronous generator is rated 50 MVA, 13.2 kV, 0.8 p.f lagging and has a synchronous reactance of 20%. The generator is connected to a 60-MVA, 13.4/138-kV, three- phase transformer having a reactance of 15%. The generator is initially operating at no load and rated terminal voltage. A three-phase fault suddenly occurs on the transformers high voltage terminals.

Choose the generator ratings as base quantities and determine:

- The short circuit current supplied by the generator.

- The generator's terminal voltage.

(14 marks)

#2	 A single line-to-ground fault occurs at point F in the system shown in Fig. 1 at rated voltage of 33 k V and no load. The apparatus ratings are as follows:

G1: 6.6 kV, 10MVA, X1=X2= 10%, Xo= 2%.

G2: 6 kV, 5 MVA, X1=X2= 5%, Xo= 3%, Xn= 4%

T: 6.6/33 k V, 15 MVA, X= 5%.

Line: X1=X2= 20 Ω, Xo= 50 Ω.

Choose a base MVA of 15 MVA and a base voltage of 33 kV in the transmission line region and calculate:

- The subtransient fault current at the fault.

- The voltage of phase c at the terminals of the two generators.

(18 marks)

# 3

A transmission link shown connects an infinite busbar supply of 33 kV, to a load busbar supplying a load of 8 MVA, 0.85 p.f lagging. The link consists of a line of effective impedance of 5 + j9 Ω feeding the load busbar  via a transformer 33/11 k V with an impedance of 1.5 + j 15 Ω referred to 33 k V, and  tap range of ± 10x1%.Calculate:

- If the supply voltage is maintained at 33 k V, Use double stage method to calculate the voltage at the load VR. Assume the transformer taps are not used, ε = 0.5 KV

- If the desired voltage at the receiving end is VR =11.5 k V find the number of tabs necessary to use on the transformer, and the real voltage that can be obtained at bus R.

- If the transformer's tabs that are determined in part (b) are fully used, calculate the reactive power required from a shunt capacitor connected to the load busbar to increase the load voltage VR to 12 kV.

(18 marks)

# Text boxes

# VS 						  VR

5 + j 9 Ω

# Supply 							    8 MVA

0.85 p.f lagging

S 				 R\      ± 10 %	    R

33/11 KV