## Slide 1: Traffic Simulator Calibration
Dr. Baker Abdalhaq

## Slide 2: Outline
Traffic simulators
Calibration
Calibration methods
  GA, TS, PS,SPSA
Some results
Further work

## Slide 3: Traffic Simulators/models
Macroscopic
  Flow -Physics
Microscopic
  Every single vehicle (physical+ behavioral)
Mesoscopic
  queue
Sub-Microscopic
  Engine rotation speed, driver gear switch…etc.

## Slide 4: Calibration
Real world
Good input -> good outputs
Some parameters are difficult to be obtained or estimated.
Calibration is optimization
simulator
output
input
Minimize
error
observations
Error (difference)
variables

## Slide 5: Calibration Methods
Classical
  Gradient based
  Simplex (Nelder-Mead, COBYLA)
Heuristic
  Genetic
  Tabu
  Particle Swarm
  SPSA

## Slide 6: Genetic
Randomly generate the first population of individuals potential solutions
Evaluate the fitness function for each population member
While not ( number of iteration reached) : obtain a new generation by repeat
  Selection of two individuals (or more)
  Crossover of selected individuals
  According the mutation probability, randomly mute the output of previous step.
  Until a new population has been completed.
end while

## Slide 7: Particle Swarm
// initial swarm usually random
for each particle :
for each dimension i
// calculate velocity
// update particle position
While stop criteria not reached, Go to step 02

## Slide 8: Simplex

## Slide 9: Taboo
Generate initial solution θ
While not finished
  identify N(θ) (Neighborhood set) by applying moves
  Identify T(θ) (tabu set)
  identify A(θ) (aspiration set)
  choose θ' in N(θ)-T(θ) U A(θ), for which f(θ') is optimal
  change θ by θ'
End wile

## Slide 10: SPSA
Step 1: Initialization
Set k=0
Pick initial guess of and nonnegative coefficients (a,c,A,α and )
Step 2: Generation of Simultaneous Perturbation Vector
Generate which is a Bernoulli distribution with probability of 0.5 for each +1 or -1 outcome
Step 3: Loss Function Evaluations
Obtain two measures of the function:
and
Step 4: Gradient Approximation
Step 5: Update estimate
Step 6: iteration or termination
If termination condition not met, return to step 2 with k+1 replacing k.

## Slide 11: SUMO input parameters
Parameter Max Min unit Description
Sigma 1 0.0 - Driver imperfection
Acceleration 0.3* 2.9* m/s^2 Ability of the car to accelerate
Deceleration 0.5* 4.9* m/s^2 Ability of the car to decelerate
Length 2 10 m Car length with leading gap
Max speed 120 10 km/h Max allowed speed

## Slide 12: Parameter Selection
Parameter | Correlation (5'000 random runs) | Parameter Importance index (PII) (formula 7) (5'000 random runs)
Length | -0.06 | 0.95
Deceleration | -0.11 | 0.86
Sigma | 0.15 | 0.84
Acceleration | -0.23 | 0.7
Max speed | -0.02 | 0.63

## Slide 13: Error Measurement

## Slide 14: Site 1

## Slide 15
Algorithm | Minimum fitness |  | Maximum fitness |  | Average fitness | Number of Fitness function executions
GA1 | 0.076 | 0.096 |  |  | 0.087 | 1250
GA2 | 0.071 | 0.105 |  |  | 0.090 | 1250
PS | 0.071 | 0.098 |  |  | 0.079 | 1034
dTS | 0.066 | 0.089 |  |  | 0.079 | 1000
sTS |  |  |  |  | 0.083 | 1000
SPSA | 0.069 | 0.077 |  |  | 0.073 | 1000
NM(Globalized) | 0.090 | 0.117 |  |  | 0.104 | 1240
COBYLA(Globalized) | 0.090 | 0.124 |  |  | 0.104 | 1220
Algorithms Performance Comparison

## Slide 16: Comparison results

## Slide 17: Site 2

## Slide 18
Algorithm | Minimum fitness | Maximum fitness | Average fitness | Number of Fitness function executions
GA2 | 0.103 | 0.184 | 0.146 | 1250
GA1 | 0.130 | 0.175 | 0.154 | 1250
PS |  |  | 0.144 | 1034
dTS |  |  | 0.166 | 1000
sTS |  |  | 0.154 | 1000
SPSA |  |  | 0.167 | 1000
NM(Globalized) | 0.164 | 0.229 | 0.187 | 1239
COBYLA(Globalized) | 0.156 | 0.205 | 0.172 | 1297

## Slide 19: Further work
Comparing Algorithms using other problems
Minimizing Co2 by changing traffic light schedule