# An-Najah National University

Faculty of Engineering 			            Elect. Engineering Department

Electrical machines 2

First exam

Date: 3- Mart-2010	 	 Duration: 1 hour    Instructors: Dr. Maher Khammash

Dr. Mu'tasem  Nour

#1.

- Draw the short circuit characteristic of the synchronous generator and explain why it is linear?

- What is the static stability limit? What happens if the synchronous generator exceeds this limit?

(5 marks)

#2. 	 A 10 MVA, 11 kV, 50 Hz, three phase, ∆-connected synchronous generator is driven at 300 rev/min. The machine has a stator with 360 slots and has 6 conductors per slot. The pitch of the stator coils is 5/6.

- Calculate the rotor flux that would be required to produce the line voltage of 11 kV on open circuit.

- Calculate the full-load current per conductor.

(8 marks)

#3.	A Y-connected, two pole synchronous generator rated at 300 kVA, 480 V,

60-Hz, and 0.8 p.f lagging. Its armature resistance RA is neglected.

The Short Circuit Characteristic is:

Field current , A	  1	  2	  3	  4	  5

Armature current , A	140	290	436	580	727

The open circuit characteristic is:

Field current, A	1.5	 2	 2.5 	3.5	4.5

Open circuit

terminal voltage, V	200	480	600	800	910

Air-gap

Terminal voltage, V	200	480	620	910	1120

- What is the saturated synchronous reactance of this generator at rated conditions?

- What is the unsaturated synchronous reactance of this generator at rated conditions?

- What is the short circuit ratio of this generator?

(7 marks)

GOOD LUCK.