# An-Najah National University

Faculty of Engineering 			            Elect. Engineering Department

Electrical machines 2

Second exam

Date: 18- April-2010	 	 Duration: 1 hour	 Instructor: Dr. M. J. Khammash

#1.     	A Y-connected, three-phase, 5 MVA, 6.6kV, 0.8 p.f lagging, and synchronous generator has a stator synchronous reactance per phase of 3.6 Ώ, and negligible armature resistance. The generator is connected to an infinite bus at 6.6 kV.

- Calculate the internal voltage EA and the torque angle when the generator is operating at rated condition.

- What is the absolute maximum amount of reactive power that the generator can supply?  Draw a phasor diagram for this condition.

(8 marks)

#2.	A three phase, Δ-connected, 500 hp, 2400-V, 60- Hz, six pole synchronous motor has a synchronous reactance of 12 Ώ per phase and is assumed to be lossless.

- Determine the induced torque when the motor operates at rated load and 0.8 p.f leading.

- If the mechanical load is now removed and the field current is unchanged, calculate the value of reactive power of the motor. Draw a phasor diagram for this condition.

(6 marks)

#3.   	A three phase, 400V, synchronous motor having a power consumption of 50kW is connected in parallel with a induction motor which takes 200kW at a p.f of 0.8 lagging.

- Calculate the current drawn from the mains when the power factor of the synchronous motor is unity.

- At what power factor should the synchronous motor operate so that the current taken from the mains is minimum?

(6 marks)

GOOD LUCK.